## Slide 1
Midterm Presentation:
— Preempt Analytics
Predicting machine failure from live sensor data — and the MLOps pipeline behind it.
Nate · Ivo | neuefische AI Engineering Bootcamp · Cohort 2026
22 May 2026 · Draft

## Slide 2
Problem & Objective

## Slide 3
Unplanned downtime is expensive
Most factories still fix machines after they break.
€thousands
lost per hour of unplanned downtime in manufacturing.
2 modes
today: react after breakage · replace on a fixed schedule.
A model that reads live sensor data and flags imminent failure changes that. Maintenance becomes intelligently planned, not reactive.
Predictive Maintenance · Midterm · Preempt Analytics
3 / 16

## Slide 4
Who uses this? — Meet Sara
Placeholder persona — to refine before final.
Sara Müller
Production Engineer at a mid-sized CNC plant.
Owns machine uptime.
Sees sensor data daily.
Buys spares on a fixed schedule.
Her challenge
Spot a failing tool before the shift ends.
Justify replacing a part now vs. next week.
Stay under €X maintenance budget per quarter.
Cost of getting it wrong
Miss a failure → unplanned line stop.
Cry wolf → wasted parts and labour.
Predictive Maintenance · Midterm · Preempt Analytics
4 / 16

## Slide 5
What we're building
Research question
To what extent can a machine learning model predict equipment failure and failure mode from real-time sensor readings — and what kind of MLOps pipeline best supports that?
Two deliverables, equal weight
The model
Classifies failure (binary) and failure mode (5-class) from sensor readings.
The pipeline
Production-grade MLOps: tracking, serving, CI/CD, monitoring.
Predictive Maintenance · Midterm · Preempt Analytics
5 / 16

## Slide 6
Data & EDA

## Slide 7
The dataset: AI4I 2020
UCI — simulated CNC machine with five failure modes.
10,000
rows · one per machine cycle
6
sensor + categorical features
~3.4%
failure rate — heavy imbalance
Sensor readings we see each cycle
air temperature · process temperature · rotational speed
torque · tool wear · machine type (L / M / H)
Engineered features so far: temp difference · power (torque × rpm) · overstrain (torque × wear) · wear % · safe-power flag · heat-dissipation risk flag.
Predictive Maintenance · Midterm · Preempt Analytics
7 / 16

## Slide 8
Five ways the machine can fail
Code | Failure | What triggers it
TWF | Tool Wear Failure | Tool exceeds wear threshold
HDF | Heat Dissipation Failure | Temp differential too low at low RPM
PWF | Power Failure | Torque × speed outside safe band
OSF | Overstrain Failure | Tool wear × torque exceeds limit
RNF | Random Failure | Unpredictable — ~0.1% of cases
RNF is the honest reminder: ~0.1% of failures we cannot predict from sensors. Our model is judged on the other four.
Predictive Maintenance · Midterm · Preempt Analytics
8 / 16

## Slide 9
The single biggest challenge: class imbalance
Chart: Failures vs non-failures (10,000 cycles)
| No failure | Failure
Cycles | 9661 | 339
So what?
Naive accuracy is useless — predicting 'no failure' every time scores 96.6%.
We track F1, precision, recall — not accuracy.
We use class-weighted XGBoost (scale_pos_weight ≈ 28).
Predictive Maintenance · Midterm · Preempt Analytics
9 / 16

## Slide 10
Modelling

## Slide 11
Two questions
— one pipeline
Binary
Will this machine fail?
Class-weighted XGBoost. Target: machine_failure.
Multiclass
If so, how will it fail?
5-way: TWF · HDF · PWF · OSF · RNF (none = no failure).
Same training pipeline. Same features. Different target. Both wired into MLflow as separate experiments.
Predictive Maintenance · Midterm · Preempt Analytics
11 / 16

## Slide 12
Where we stand today
Binary XGBoost · test set · 20% holdout
0.64
F1 (test)
0.64
Precision (test)
0.65
Recall (test)
Reading the numbers
We catch roughly 2 out of every 3 failures, and 2 of every 3 alerts are real.
Solid baseline — but not yet good enough for Sara to trust unsupervised.
LightGBM + Optuna tuning + better features are the next levers (see Outlook).
Predictive Maintenance · Midterm · Preempt Analytics
12 / 16

## Slide 13
The MLOps Pipeline

## Slide 14
The pipeline is the deliverable
Data → Experiments → Serving → CI/CD → Monitoring
01
Data
DVC
02
Experiments
MLflow
03
Serving
FastAPI · Docker
04
CI/CD
GitHub Actions
05
Monitoring
Prometheus · Grafana
Status (today)
Done DVC scaffolding · MLflow tracking · binary + multiclass experiments
In progress FastAPI service · Dockerised inference · model registry promotion
Next GitHub Actions CI · Prometheus + Grafana dashboard
Predictive Maintenance · Midterm · Preempt Analytics
14 / 16

## Slide 15
What's next
Plain-spoken limits and what we plan to do about each.
Limitation today | Next step
F1 plateau at ~0.64 on the binary task | Optuna tuning across LightGBM + XGBoost; ensemble of seeds.
Multiclass underperforms on rare modes (RNF) | Per-class metrics; threshold tuning; consider one-vs-rest.
No live serving yet | Wrap best model in FastAPI; containerise; smoke-test locally.
No drift / monitoring | Add Prometheus exporters and a Grafana dashboard.
Single static dataset | Discuss streaming/simulated drift for the final.
Predictive Maintenance · Midterm · Preempt Analytics
15 / 16

## Slide 16
Thank you
Questions, pushback, and ideas — all welcome.
Preempt Analytics
Nate · Ivo
neuefische AI Engineering Bootcamp · Cohort 2026